OAKLAND UNIVERSITY

BOARD OF TRUSTEES

WORKING SESSION AGENDUM ITEM

March 5, 2003

# AUTHORIZATION TO PROCEED WITH SURFACE REPAIR OF PARKING LOT 36

Division/Department:  Finance and Administration/Facilities Management

Summary:

Parking Lot 36 is a large lot, with nearly 500 spaces, located between the Science and Engineering Building (SEC) and Elliott Hall (EH).  The pavement condition on the lot has deteriorated to the point that repair is required to preclude additional serious damage.  Severe cracking has occurred over the majority of the lot and the pavement has failed in some areas, resulting in surface breakdown and exposed soil conditions.  The project would involve mechanically pulverizing the entire pavement area and

re-compacting the material, completely rebuilding about 1,700 square yards of failed pavement area, rebuilding of 8 storm water catch basins, and installation of a 3” asphalt wearing surface over the entire lot.

Action to be Requested at Next Formal Board Meeting:

Authorization for the Vice President for Finance and Administration to execute a contract with the lowest responsible bidder for the surface repair of Parking Lot 36.  The contract will be reviewed and approved by the Office of General Counsel prior to execution, and will be in compliance with the law and University policies and regulations and shall conform to the legal standards and policies of the Board of Trustees.

Budgetary Implications:

Total project would not exceed $300,000.  The funding source would be the Parking Fund.

Reviewed by Secretary Victor A. Zambardi:		__________

(Please Initial)

## Reviewed by President Gary D. Russi:		__________

(Please Initial)

# Agendum

Oakland University

Board of Trustees

April 2, 2003

APPROVAL TO PROCEED WITH SURFACE REPAIR OF PARKING LOT 36

# A Recommendation

### Introduction:

Parking Lot 36 is a large lot, with nearly 500 spaces, located between the Science and Engineering Building and Elliott Hall.  The pavement condition on the lot has deteriorated to the point that repair is required to preclude additional serious damage.  Severe cracking has occurred over the majority of the lot and the pavement has failed in some areas, resulting in surface breakdown and exposed soil conditions.  The project would involve mechanically pulverizing the entire pavement area and re-compacting the material, completely rebuilding about 1,700 square yards of failed pavement area, rebuilding of 8 storm water catch basins, and installation of a 3” asphalt wearing surface over the entire lot.

### Recommendation:

RESOLVED, that the Vice President for Finance and Administration be authorized to execute a contract with the lowest responsible bidder for the surface repair of Parking Lot 36; and, be it further

RESOLVED, that the contract shall be reviewed and approved by the Office of the General Counsel prior to execution and shall be in compliance with the law and University policies and regulations and shall conform to the legal standards and policies of the Board of Trustees; and, be it further

# RESOLVED, that the project budget shall not exceed $300,000.

#### Budgetary Implications:

# Funding is proposed from the Parking Fund.

# Submitted to the President

on __________________, 2000 by

____________________________

# Lynne C. Schaefer

Vice President for Finance and Administration

and Treasurer to the Board of Trustees

# Recommended on ______________, 2000

to the Board for approval by

____________________________

# Gary D. Russi

President